## AGT 16503 HSBE

## THREE PHASE GENSET

ALTERNATOR

Type:					Synchronous, brushes, three phase

Max. power:				16 kVA (3~) / 8 kVA (1~)

Power factor:				0,8 (3~) / 1 (1~)

ENGINE				HONDA

Type:					2 cylinders, air cooled, OHV

Model:				GX 690 Euro2, New V-Twin

Bore x stroke:			78 x 72 mm

Displacement:			688 cm3

Compression:			9,3:1

Max. power:				25,6 HP

Ignition system:			Digital CDI with variable ignition timing

Combustion chamber:		Hemispherical

Carburetor:				2-barrel, fuel cut solenoid, inner vent

Air filter:				Dual Element Type/Cylindrical

Fuel:					Unleaded gasoline

Starting system:			Electric

gENeRATING SET

Voltage:				400 V (3~) / 230 V (1~) / 50 Hz

Max. power (LTP):			15.5 kVA (3~) / 8 kVA (1~)

Continuous power (COP):	13.1 kVA (3~) / 6.8 kVA (1~)

Speed:				3.000 rpm

Consumption:			4 l/h at 75% load

Protection degree:			IP 23

Overall dimensions:		880x575x705 mm(L x l x h)

Fuel tank capacity:			16,0 l

Weight:				126 kg

Standard equipment:

One single phase 16 A Schuko socket

One single phase 32 A CEE type socket

One three phase 32 A CEE type socket

Circuit breaker

Oil alert protection

Hour meter

Fuel level gauge

Magnetothermal switch

Electric starter and keyswitch

35Ah battery and charger

Optional:		RCBO 15,5KVA (3~) / 5 kVA (1~)

Automatic panel

Wheels and handles

4 handles system